## Slide 1: F1 QUALIFYING TRACKER
By Palin Wiseman

## Slide 2: Design process
A device to improve my Formula 1 watching experience
First concept: All 20 drivers, all sectors, all mini-sectors
Scope was way too big; device would have taken up my entire desk (and cost a lot)
Refocused on qualifying and tracking
Temporary case and breadboard as I am continuing development after semester

## Slide 3: Tech - PC
Streaming F1TV through MultiViewer
  Running at least a commentary stream and a Live Timing stream
  Race, qualifying, or practice
  Live or replay
Running a Flask app API
  Uses mvf1 python package by Rob Spectre
  Getting driver data from MultiViewer
  Posting driver to open perspective cam
Hosted with ngrok

## Slide 4: Tech – Raspberry Pi 4
Running a python script
Uses requests package to interact with the API
  Requests driver data
  Posts driver number to focus on
Wired serial connection to the Arduino
  Uses multithreading to read and write at the same time
  Sends driver data to be displayed
  Accepts button inputs to set new focused driver
Starts when plugged in and can recover from Arduino disconnection

## Slide 5: Tech – Arduino Uno
Wired serial connection to Pi
  Accepts driver data and mini-sector information
  Sends driver number when button is hit
6 buttons, one for each driver
3 LCD screens, 2 drivers on each
  Displays position, team, and name
6 strips of 5 LEDs
  Most recent 5 mini-sectors for each driver this lap

## Slide 6: The future?
3D printed case
Soldered circuit board
Improved code
  Customize where windows open
  Different driver selection logic for races
More displays
  Session time
  LED Matrix display for racing condition flags
  Laps remaining